## Slide 1
Capture and Ligation Probe-PCR
(CLIP-PCR) for Molecular Screening,
with Application to Active Malaria
Surveillance for Elimination
Z. Cheng, D. Wang, X. Tian, Y. Sun, X. Sun,
N. Xiao, and Z. Zheng
June 2015
www.clinchem.org/content/61/6/821.full
© Copyright 2015 by the American Association for Clinical Chemistry

## Slide 2: Introduction
  Malaria control programs have made remarkable success over the past decade, but challenges remain
    111 countries eliminated malaria
    34 countries approaching elimination
  Elimination requires active screening to find all infections in a timely manner
  Asymptomatic parasitic reservoir is now a major hurdle, accounting for up to 50% of all transmissions in low-endemic areas

## Slide 3: Introduction
  Active screening adds significant resource burdens
    As prevalence approaches elimination, a greater number of tests have to be performed to find one infection
    Tests are free-of-charge to ensure participation
  Current clinical diagnostics are inadequate for asymptomatic infections
    WHO recommendations are Microscopy or immunological Rapid Diagnostic Test (RDT), which cannot detect below 40-50 parasites/μL blood.
    Active case detection using RDT did not reduce parasite prevalence(1)
  PCR has the sensitivity (0.5 parasites/μL), but is not practical for screening due to high cost and low throughput
  Study aim was to develop a high-throughput PCR detecting genus-specific 18s rRNA, suitable for dried blood spot (DBS) samples.
Tiono AB, et al. A controlled, parallel, cluster- randomized trial of community-wide screening and treatment of asymptomatic carriers of Plasmodium fal- ciparum in Burkina Faso. Malar J 2013;12:79.

## Slide 4: Question
Is automated DNA/RNA extraction the solution to adapt PCR for high-throughput malaria screening?

## Slide 5
Used laboratory-cultured Plasmodium falciparum (isolate 3D7) samples to test the analytical performances of our method
Tested 3358 dried blood spots collected in active screenings from 3 low-endemic areas
  Cohort 1: 505 from Gengma County, including 279 children. None symptomatic on sampling day, 2 with history of P.vivax infection in the past 6 months
  Cohort 2: 2064 from Tengchong County, including 914 migrant workers returned from malaria-endemic Myanmar
  Cohort 3: 789 from Feidong County, including 69 returned from malaria-endemic Africa.
  All samples tested with microscopy and our method, Cohort 1 also tested with RDT
  Standard Taqman qPCR as gold standard
Materials and Methods

## Slide 6
CLIP-PCR Workflow
Notes
One 3mm punch from each DBS
Each sample tested once in row pool and once in column pool
Probes aligned and ligated only in the presence of target
Unbound probes washed off before ligation
Target and ligated template anchored at the bottom, not in the solution
Capture, ligation and qPCR in the same well
qPCR with SYBR Green

## Slide 7: Additional Questions
What makes this assay capable of high-throughput?
What features of the assay provide good sensitivity?
How does the assay ensure specificity?
What is one benefit of target/PCR template anchored at the bottom and not in solution?
What is the benefit of using universal primers?

## Slide 8: CLIP-PCR can detect as low as 0.01 parasites/μL
Serial dilution of 3D7 blood lysate
Specific and non-specific product melting peaks well separated
Positive identification: (1) Cq<40 and (2) specific melting peak

## Slide 9: CLIP-PCR detects targets in pooled DBS samples with little loss of signal
Chart: Pooling size
| single DBS | 11 | 21 | 26 | 36 | re-elution of 36
 | 28.35 | 28.32 | 28.725 | 28.555 | 28.85 | 30.12
Detection of P. falciparum by use of DBS with varying pool sizes. DBSs were prepared by spotting 75 μL of either cultured P. falciparum strain 3D7 or whole blood from healthy volunteers to Whatman 3MM filter paper and air-drying for 4 h. Single-positive DBS (50 parasites/μL) was mixed with 0, 10, 20, 25, or 35 negative DBSs separately and tested as a single sample by CLIP-PCR. Pools of ≤26 were tested in duplicate, whereas a lysate of pool size 36 was sufficient for only 1 test; additional elution with 100 μL lysis mixture was used for the second test.

## Slide 10: Question
Why does the pooling of samples have little influence on the Cq value?

## Slide 11: Finding asymptomatic infections in active screening*
a Mean (SD) based on duplicate tests.b Whole blood sample. c–f Patient developed malaria-related syndrome after sampling. g DBS.h NA, not tested.
*CLIP-PCR finished screening of 3358 samples with <500 tests, costing $0.6/ sample
From
Cohort 1
From
Cohort 2

## Slide 12: CLIP-PCR is Ideal for Active Malaria Screening
  Sensitive and specific
      LOD of 0.01parasites/μl, equivalent to RT-PCR
      Finds asymptomatic infections missed by current methods and false-positives by RDT
  High throughput
      no need for extraction and reverse transcription
      pool size of up to 26
      up to thousands DBS samples per person run
  Low cost
      without extraction cost
      qPCR with Sybr green chemistry
      pooling
Editorial by Zimmerman PA. Nucleic Acid Surveillance and Malaria Elimination. Clin Chem 2015; 61:789-791.
http://www.clinchem.org/content/61/6/789.full

## Slide 13: CLIP-PCR for Molecular Diagnostics
  Versatile
      Any pathogen with ~100bp contiguous specific sequence can potentially be targeted
      RNA or DNA target
  Centralized, high-throughput testing
      Good for screening a large number of specimens
      Blood/DBS, swab or other sample types
      Target on DBS stable at RT for at least 2 weeks
  Multiplex capability
      Can use probe-based multicolor detection or other detection approaches.
      Universal primers amplify different targets equally