## Slide 1
Clinical Evaluation of a Blood Assay to Diagnose Paucibacillary Tuberculosis Via Bacterial Antigens
C. Liu, C.J. Lyon, Y. Bu, Z. Deng, E. Walters, Y. Li, L. Zhang, A.C. Hesseling, E.A. Graviss, and Y. Hu
April 2018
http://clinchem.aaccjnls.org/content/64/5/791
© Copyright 2017 by the American Association for Clinical Chemistry

## Slide 2: Introduction
Background
  Diagnosis of active tuberculosis (TB) cases relies on methods that detect Mycobacterium tuberculosis (Mtb) bacilli or their DNA (e.g., mycobacterial culture and Xpert MTB/RIF assays)
  Bacteriologic and molecular assays used for TB diagnosis exhibit suboptimal clinical sensitivity in patients with low mycobacterial loads or poor sputum production (e.g. most HIV-positive and pediatric patients).
  Mtb-derived virulence factors (e.g. CFP-10 and ESAT-6) may represent good diagnostic markers for active TB but cannot be reliably detected with current methods
Objective
  To evaluate the clinical performance of a new assay that can rapidly diagnose active TB cases by direct detection of Mtb-derived antigens in patients’ blood samples

## Slide 3: Introduction - Question:
What are the current limitations of assays used to diagnose active TB cases and why might a blood-based liquid biopsy approach be preferable?

## Slide 4: Methods - Study Overview
  Methods:
  Nanoparticles (NanoDisks) coated with antibodies to Mtb-specific peptides of the mycobacterial virulence factors CFP-10 and ESAT-6 were employed to enrich these factors from digested serum samples
  After hybridization, loaded NanoDisks were analyzed using a high-throughput mass spectrometry (MS) system to identify and quantify CFP-10 and ESAT-6 with high analytical sensitivity and specificity
  Direct measurement of serum levels of Mtb peptides was used to diagnose active TB cases
  Study design:
  Serum from 294 prospectively enrolled Chinese adults was analyzed by NanoDisk-MS to evaluate the potential utility of direct measurement of serum Mtb antigen levels to rapidly diagnose active TB cases

## Slide 5
Methods - Subject Enrollment
Figure 1. Participant disposition flow chart. NTM = nontuberculous mycobacteria

## Slide 6
Methods - Technology Overview
Figure 2. NanoDisk-MS assay procedure. Serum samples of suspected TB cases are trypsin digested and incubated with antibody-functionalized NanoDisk particles that bind Mtb specific peptides (A). Serum Mtb CFP-10 and ESAT-6 concentration are determined by the mass spectra intensity ratios of the Mtb target peptides (1593.75 and 1900.95 m/z) and their isotope-labeled internal standards, respectively. Representative NanoDisk-MS results for the peaks of interest from a clinically confirmed active TB case and a control subject with a negative TB diagnosis (B).

## Slide 7: Method - Question:
What are the advantages and limitations conferred by using an assay that employs an affinity nanoparticle to detect a disease-specific peptide?

## Slide 8: Results - Summary

## Slide 9
Results - Serum CFP-10 and ESAT-6 Concentrations
Figure 3. Serum CFP-10 (red) and ESAT-6 (green) concentrations (CFP-10 + ESAT-6) in each clinically confirmed TB case, with patients grouped according to their Mtb culture status and disease site.

## Slide 10
Results - Sensitivity in Mtb Culture and AFB Negative Patients
Supplemental Table 1. NanoDisk-MS diagnostic sensitivity for patients with positive and negative Mtb culture and AFB smear results.

## Slide 11
Results - In Different TB Subgroups
Figure 3. NanoDisk-MS results in different TB subgroups. Mtb culture-positive vs culture-negative cases (A). AFB smear-positive vs smear-negative cases (B). Mtb culture-positive and culture-negative pulmonary and extrapulmonary TB cases and non-TB cases (C). Data points indicate the NanoDisk-MS readout for each study participant, while black lines indicate the median and interquartile range. NanoDisk-MS readout is the combined CFP-10 and ESAT-6 concentration.

## Slide 12: Results - Analytical Validation

## Slide 13: Results - Questions:
How might the NanoDisk-MS assay, pending further validation studies, provide value to TB management and what factors may constrain its utility?
What appear to be the current limitations of the NanoDisk-MS assay sensitivity and specificity, particularly with regard to NTM and latent TB cases, and what studies need to be performed to address these issues?

## Slide 14: Summary and conclusions
Current Technology
Current TB assays exhibit suboptimal sensitivity in TB patients with low mycobacterial loads or poor sputum production (e.g. most HIV-positive and pediatric TB patients)
NanoDisk-MS:
  NanoDisk-MS accurately detected CFP-10 and/or ESAT-6 in the serum of active TB cases across all subgroups in this study, achieving 88.3% clinical sensitivity and 95.8% specificity
  Sensitivity did not differ for pulmonary vs extrapulmonary TB, nor was it affected by culture or AFB status
  NanoDisk-MS provides quantitative results, unlike current frontline diagnostics
Conclusions:
  This blood-based biomarker approach has the potential to improve TB diagnosis in diagnostically challenging patient cohorts
  Longitudinal NanoDisk-MS results may be useful for rapid evaluation of treatment responses and predicting clinical outcomes of TB patients

## Slide 15: Key points from the Lori Bourassa editorial
Rapid and accurate diagnosis of active TB and initiation of treatment are critical to control the spread of disease.
  AFB is fast and inexpensive, but less sensitive
  Culture (gold standard) is more sensitive than AFB, but may take up to 8 weeks
  GeneXpert MTB/RIF improves speed and sensitivity, and can detect rifampin resistance. However, it is only approved for the diagnosis of pulmonary TB and has higher analytical sensitivity in smear-positive than in smear-negative patients
WHO has identified the development of a nonsputum-based biomarker test as a priority.
  NanoDisk-MS is “a blood-based biomarker assay that holds promise for the detection of pulmonary TB and EPTB and for use in measuring response to treatment”
  Clinical performance assessment in 376 HIV-negative adults in China shows that “the assay vastly outperformed both AFB smear microscopy and culture, detecting ESAT-6 or CFP-10 peptide in 85.3% of culture-negative and 87.2% of smear-negative cases.”
  Future studies:
    Assessment of performance in children and in those with latent TB infection
    Address the major limitation for point-of-care test applications