## Slide 1
Liquid Biopsy Hotspot Variant Assays: Analytical Validation for Application in Residual Disease Detection and Treatment Monitoring
A. Hallermayr, A. Benet-Pagès, V. Steinke-Lange, U. Mansmann, M. Rentsch, E. Holinski-Feder, J.M.A. Pickl
November 2021
https://doi.org/10.1093/clinchem/hvab124
© Copyright 2021 by the American Association for Clinical Chemistry

## Slide 2
Tumor variants in plasma can be analyzed for a variety of clinical applications. Highly sensitive tumor variant analysis can be performed by digital droplet PCR.
% Tumor variant
in plasma
time
diagnosis
surgery
recurrence
therapy
Residual
disease
Therapy
decision
Resistance
development
Therapy
monitoring
Residual disease
1 copy per droplet
20,000 droplets
Tumor variants in plasma
Droplet Digital PCR (ddPCR)

## Slide 3
Tumor variants with therapy relevance in non-small cell lung cancer (NSCLC), melanoma, and colorectal cancer can be analyzed using liquid biopsy
Tumor variant
NSCLC Melanoma Colorectal cancer
EGFR p.T790M
EGFR p.L858R
EGFR Exon 19 deletion
KRAS p.G12/p.G13
BRAF p.V600E

## Slide 4
time
Technical challenges in liquid biopsy
LOB and LOQ determination is required for accurate tumor variant identification and quantification
≥ Limit of Blank (LOB)
> Limit of Quantification (LOQ)
% Tumor variant
in plasma
diagnosis
surgery
recurrence
therapy
Residual
disease
Therapy
decision
Resistance
development
Therapy
monitoring
Residual disease
Identification of tumor variants with very low frequency in plasma: Limit of Blank (LOB)
Precise tumor variant quantification in plasma: Limit of Quantification (LOQ)
Even very low frequency variants (<1%) serve as indicator for residual disease and response to EGFR-directed therapy

## Slide 5: Introduction summary
Liquid biopsy is a promising tool for identification of genetic tumor status and real-time monitoring of evolutionary tumor dynamics in plasma.
Detection and quantification of pathogenic KRAS, BRAF, and EGFR variants in liquid biopsy may be used to detect therapy resistance, residual disease, and recurrence before clinical evidence, in different types of solid cancer.
In liquid biopsy, highly sensitive methods including ddPCR and in-depth validation of the lower end of the measurement scale are required to detect lowest amounts of variants in plasma, and to distinguish their signals from inherent background noise, since these are relevant for individual treatment decision.
QUESTION: What may be advantages of liquid biopsy compared to tissue biopsy?

## Slide 6: Materials & Methods
Determination for each liquid biopsy assay whether a result was truly negative, positive (using LOB), and quantifiable (using LOQ) – according to CLSI guidelines
Further evaluation of parameters including total measurement error, trueness, precision, and linearity.
Positive controls: Dilution series of DNA reference material was generated (mutant variant allele frequency [VAF] range 0.05% to 100%)
Negative controls: gDNA from whole blood and cell-free DNA (cfDNA) from plasma pools of healthy individuals were used. All individuals provided written informed consent.
LOB: > 75 negative controls measurements
LOD: > 60 positive control measurements of very low mutant VAF positive control samples
LOQ: > 40 positive control measurements of very low mutant VAF positive control samples
Linearity: 7 positive control samples in 2-3 replicates from LOQ to 100% VAF
QUESTION: Which performance characteristics should be taken into account when accurately quantifying tumor variants in plasma?

## Slide 7
Technical challenges in liquid biopsy
Determination of the LOB for each single assay to detect a tumor variant using negative control samples
When applying these methods for clinical interpretation, it is critical to understand and assess their performance characteristics at the lower end of the measurement scale.
Measurement number
Assay-specific dispersion
Limit of Blank
5% False Positive Rate
Cutoff for presence of a tumor variant (95% specificity)
0.00%
0.75
% Tumor variant in plasma

## Slide 8
Technical challenges in liquid biopsy
Determination of the LOQ for each single assay to precisely quantify a low frequency tumor variant using positive control samples
5% Falsch Negativ
Rate
5% False Positive Rate
Limit of Quantification
Limit of Detection
≥ 95% Sensitivity
≥ 95% Specifity
0.00%
0.75
Limit of Blank
5% False Negative
Rate
Measurement number
% Tumor variant in plasma
Assay-specific dispersion
Limit of Detection and ≤ Total Error Goal
Tumor variant frequency quantifiable

## Slide 9
LOB, LOD & LOQ of five ddPCR assays
Assay-specific performance characteristics for analysis of low-frequency tumor variants
% Tumor variant in plasma
Each assay has different performance characteristics
Differences must be considered in clinical reporting
Clinically relevant LOB and LOQ are not commonly reported by liquid biopsy assay providers
not defined
not defined

## Slide 10
Performance characteristics differ between tumor variant frequencies and assays at LOQ, < 10% and ≥ 10%

## Slide 11
Application of LOB and LOQ thresholds in clinical use
Example: Follow-up circulating-free DNA (cfDNA) samples of two patients with colorectal cancer having either the KRAS p.G13D variant or the BRAF p.V600E variant present in tumor tissue were analyzed at different time points throughout the course of disease

## Slide 12
Guide for clinical interpretation of circulating tumor DNA (ctDNA) analysis results, dependent on determined LOB and LOQ.
An exemplary course of disease with several clinical decisions to be made.
During treatment and follow-up of patients with cancer, both ctDNA detection (negative ≤LOB, positive >LOB) and ctDNA quantification (possible ≤ LOQ) of mutant variants supports clinical decisions for treatment.

## Slide 13
Summary
Determination of clinically relevant cutoffs LOB and LOQ is not common in commercial liquid biopsy testing
The analytical validation performed within this study enabled precise differentiation between negative and positive results (LOB) and quantification of the VAF (above the LOQ).
Applied liquid biopsy assays in this study were highly sensitive when compared to other liquid biopsy assays (LOD)
Applying the liquid biopsy, tumor progression and response to treatment in two exemplary clinical samples was oberved.
There are assay-specific cutoffs for tumor variant detection and quantification, highlighting the need for determining these performance characteristics for each single mutant variant assay individually to enable precise clinical interpretation for each variant.
Abilty to provide a comprehensive actionable report for patients and enable disease monitoring.
QUESTION: How can LOB and LOQ cutoffs help to guide clinical decisions?